## Slide 1: Sliding window technique with code implementation
CSE-350
Data Communications
Section 01
Presented by:
Rajashree roy/2014-3-60-070
ALINOOR HOSSAIN OLIP/2014-3-60-008

## Slide 2: Overview
Transmission Mode
Asynchronous & Synchronous
Synchronous mode variation
Sliding Window
Implementation
Pros & Cons
Real world example
Conclusion

## Slide 3: Introduction
Asynchronous:
It is asynchronous if the system allows the physical medium to be idle for an arbitrary time between two transmissions
The asynchronous style of communication is well-suited to applications that generate data at random
  (e.g., a user typing on a keyboard or a user that clicks on a link)
The disadvantage of asynchrony arises from the lack of coordination between sender and receiver

## Slide 4
Synchronous:
A synchronous mechanism transmits bits of data continually
  with no idle time between bits
  after transmitting the final bit of one data byte, the sender transmits a bit of the next data byte
The sender and receiver constantly remain synchronized
  which means less synchronization overhead
  Needs to control the flow
8 bit Control Data Control 8 bit
Flag Field Field Field flag

## Slide 5: Flow control
Widely known two technique
Stop and Wait
Sliding Window
Stop and wait:
Takes only one frame
Doesn’t know the buffer size
Flow prevention is hundred percent

## Slide 6: Can we do even better?
In Stop and Wait, only 1 frame outstanding at any given point in time.
What’s the problem with that?
  “Loooong pipes”.
  Channel
  S R
  Time consuming
  Inefficient

## Slide 7: Sliding Window
Window: number of “outstanding” frames at any given point in time.
  So what’s the window size of Stop and Wait?
Every ACK received, window slides.

## Slide 8: Sliding Window: Basics
Allows multiple frames to be in transit at the same time.
Receiver allocates buffer space for n frames.
Transmitter is allowed to send n (window size) frames without receiving ACK.
Sequence number?
2 bit control Data field 11 bit FCS 3 bit
sequence no.

## Slide 9: Sliding Window: Receiver
Receiver maintains window corresponding with frames it can receive.
Receiver ack’s frame by including sequence number of next expected frame.
  Cumulative ACK: ack’s multiple frames.
Example: if receiver receives frames 2,3, and 4, it sends an ACK with sequence number 5, which ack’s receipt of 2, 3, and 4.

## Slide 10
Example: window size 3
0
1
2
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
ACK 3
0 1 2 3 4 5 6 7 0 1 2 3 4
3
4
5
ACK 6
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
0 1 2 3 4 5 6 7 0 1 2 3 4
A (Sender) B (Receiver)
0 1 2 3 4 5 6 7 0 1 2 3 4… 0 1 2 3 4 5 6 7 0 1 2 3 4

## Slide 11: Pros & cons
Efficiently uses the link
Timing error is less
More frame gives better synchronization
Complex to design
Need many technique to keep synchronization
Error prone

## Slide 12: Real life examples
VOIP Calls (voice over internet protocol)
Chatroom
Any transmission media that needs to communicate frequently

## Slide 13: Project Limitations
No input system
Limitations of data size
No ARQ used

## Slide 14: Conclusion
Sliding window is efficient. It got less overhead.
Instead of some design complexity and error it’s a very good technique for responsive communication.